## Slide 1: Project Presentation
Team ID : Group 15
System Integrator : Chia Kok Bond (30893062)
Programmer : Mah Yuen Yee (30213673)
Notes: System block 2.5min
Crucial aspects 1.1min
Movement 3.3min
Colour 1.7min
Puck 2.1min
Alternative 1min

## Slide 2
K
I
S
S
Keep It Short And Simple
Keep It Fast And Simple

## Slide 3: Presentation Structure
01 System Overview (CKB)
  System Block Diagram
  Crucial Aspects of Design
02 Design Methodology
  Motion Flow & Key Methods
  Movement mechanism (MYY)
  Colour Sensing mechanism (MYY)
  Puck Handling mechanism (CKB)
03 Decision Making (MYY)
  Unused Alternative Design
04 Conclusion (CKB)

## Slide 4: 01 System Overview
System Block Diagram
Crucial Aspects of Design
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making

## Slide 5
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making

## Slide 6
Colour Sensing Subsystem
Puck Handling Subsystem
Movement Subsystem
State Sequence Initiation Subsystem
Fig. 1 System block diagram.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Fig. 1 System block diagram.
Notes: To handle all aspects of tasks provided in this project, there are 4 main subsystems implemented in the robot which are colour sensing, puck handling, movement, and state sequence initiation subsystems.
First is about the colour sensing subsystem. Its algorithm outputs 2 types of signals to the 2 TCS3200 colour sensors, one to switch on and off the attached LEDs, the other is for activation of photodiodes with filter of different colours. The algorithm receives input signal of square wave with different frequency to determine puck colour.
Secondly, it’s about the puck handling subsystem. The algorithm outputs analogue signal of pulse width modulator compare value which represents the duty cycle for angular positioning of servo rod to any of the 4 SG90 plastic gear servo motors. The servo motor would then rotate its rod accordingly to flick puck.
Next is the movement subsystem. The algorithm sends signals to the motor driver to inform the intended rotating speed and direction of the wheels to move and stop the robot. The motor driver then outputs the information to the DC motors by changing voltage supplied. Each DC motor has its shaft attached to a gearbox which is connected to a wheel so that the DC motor shaft and the wheel has the same speed and direction. The shaft encoder attached to each DC motor can indirectly capture the angular displacement of the wheel. The signals are then fed back into the algorithm consistently to enable motion control, speed control and differential drive control.
The fourth is the state sequence initialization subsystem. A press of the reset button on the PSoC board signals the algorithm to reset the robot to be in the initial idle state. The on-board push button can then be pressed to inform the algorithm to traverse from the initial idle state to state 2 to kickstart the robot activities.
Lastly, 12 3000mAh Ni-MH rechargeable batteries are used to supply 14.4V which is stepped down to 12V by a DC-DC buck convertor (Full name)to power DC motors via motor driver. The 12V is then stepped down again to 5V to power the remaining electronics.
~2.3m

## Slide 7
Colour Sensing Subsystem
Fig. 1 System block diagram.
Colour Sensing Subsystem
Fig. 2 TCS3200 colour sensor [1].
LEDs
Photodiodes
Fig. 3 TCS3200 colour sensor block diagram [2].
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Fig. 1 System block diagram.
Notes: To handle all aspects of tasks provided in this project, there are 4 main subsystems implemented in the robot which are colour sensing, puck handling, movement, and state sequence initiation subsystems.
First is about the colour sensing subsystem. Its algorithm outputs 2 types of signals to the 2 TCS3200 colour sensors, one to switch on and off the attached LEDs, the other is for activation of photodiodes with filter of different colours. The algorithm receives input signal of square wave with different frequency to determine puck colour.
Secondly, it’s about the puck handling subsystem. The algorithm outputs analogue signal of pulse width modulator compare value which represents the duty cycle for angular positioning of servo rod to any of the 4 SG90 plastic gear servo motors. The servo motor would then rotate its rod accordingly to flick puck.
Next is the movement subsystem. The algorithm sends signals to the motor driver to inform the intended rotating speed and direction of the wheels to move and stop the robot. The motor driver then outputs the information to the DC motors by changing voltage supplied. Each DC motor has its shaft attached to a gearbox which is connected to a wheel so that the DC motor shaft and the wheel has the same speed and direction. The shaft encoder attached to each DC motor can indirectly capture the angular displacement of the wheel. The signals are then fed back into the algorithm consistently to enable motion control, speed control and differential drive control.
The fourth is the state sequence initialization subsystem. A press of the reset button on the PSoC board signals the algorithm to reset the robot to be in the initial idle state. The on-board push button can then be pressed to inform the algorithm to traverse from the initial idle state to state 2 to kickstart the robot activities.
Lastly, 12 3000mAh Ni-MH rechargeable batteries are used to supply 14.4V which is stepped down to 12V by a DC-DC buck convertor (Full name)to power DC motors via motor driver. The 12V is then stepped down again to 5V to power the remaining electronics.
~2.3m

## Slide 8: System Block Diagram
Colour Sensing Subsystem
Puck Handling Subsystem
Movement Subsystem
State Sequence Initiation Subsystem
Fig. 1 System block diagram.
Fig. 6 180-degree SG90 plastic gear servo motor [4].
Fig. 7 Servo motor with a rod attached.
Fig. 4 Input and output pins of SG90 plastic gear servo motor [3].
Fig. 5 PWM compare value controls duty cycle.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Subsystem
Fig. 1 System block diagram.
Notes: To handle all aspects of tasks provided in this project, there are 4 main subsystems implemented in the robot which are colour sensing, puck handling, movement, and state sequence initiation subsystems.
First is about the colour sensing subsystem. Its algorithm outputs 2 types of signals to the 2 TCS3200 colour sensors, one to switch on and off the attached LEDs, the other is for activation of photodiodes with filter of different colours. The algorithm receives input signal of square wave with different frequency to determine puck colour.
Secondly, it’s about the puck handling subsystem. The algorithm outputs analogue signal of pulse width modulator compare value which represents the duty cycle for angular positioning of servo rod to any of the 4 SG90 plastic gear servo motors. The servo motor would then rotate its rod accordingly to flick puck.
Next is the movement subsystem. The algorithm sends signals to the motor driver to inform the intended rotating speed and direction of the wheels to move and stop the robot. The motor driver then outputs the information to the DC motors by changing voltage supplied. Each DC motor has its shaft attached to a gearbox which is connected to a wheel so that the DC motor shaft and the wheel has the same speed and direction. The shaft encoder attached to each DC motor can indirectly capture the angular displacement of the wheel. The signals are then fed back into the algorithm consistently to enable motion control, speed control and differential drive control.
The fourth is the state sequence initialization subsystem. A press of the reset button on the PSoC board signals the algorithm to reset the robot to be in the initial idle state. The on-board push button can then be pressed to inform the algorithm to traverse from the initial idle state to state 2 to kickstart the robot activities.
Lastly, 12 3000mAh Ni-MH rechargeable batteries are used to supply 14.4V which is stepped down to 12V by a DC-DC buck convertor (Full name)to power DC motors via motor driver. The 12V is then stepped down again to 5V to power the remaining electronics.
~2.3m

## Slide 9: System Block Diagram
Colour Sensing Subsystem
Movement Subsystem
State Sequence Initiation Subsystem
Fig. 1 System block diagram.
Fig. 9 L298N motor driver [6].
Fig. 10 Transfer plate [7].
Fig. 8 DC motor with shaft encoder [5].
Puck Handling Subsystem
Gearbox
DC motor with attached shaft encoder
Wheel
Spinning rod
Fig. 11 Wheel set.
Movement Subsystem
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Fig. 1 System block diagram.
Notes: To handle all aspects of tasks provided in this project, there are 4 main subsystems implemented in the robot which are colour sensing, puck handling, movement, and state sequence initiation subsystems.
First is about the colour sensing subsystem. Its algorithm outputs 2 types of signals to the 2 TCS3200 colour sensors, one to switch on and off the attached LEDs, the other is for activation of photodiodes with filter of different colours. The algorithm receives input signal of square wave with different frequency to determine puck colour.
Secondly, it’s about the puck handling subsystem. The algorithm outputs analogue signal of pulse width modulator compare value which represents the duty cycle for angular positioning of servo rod to any of the 4 SG90 plastic gear servo motors. The servo motor would then rotate its rod accordingly to flick puck.
Next is the movement subsystem. The algorithm sends signals to the motor driver to inform the intended rotating speed and direction of the wheels to move and stop the robot. The motor driver then outputs the information to the DC motors by changing voltage supplied. Each DC motor has its shaft attached to a gearbox which is connected to a wheel so that the DC motor shaft and the wheel has the same speed and direction. The shaft encoder attached to each DC motor can indirectly capture the angular displacement of the wheel. The signals are then fed back into the algorithm consistently to enable motion control, speed control and differential drive control.
The fourth is the state sequence initialization subsystem. A press of the reset button on the PSoC board signals the algorithm to reset the robot to be in the initial idle state. The on-board push button can then be pressed to inform the algorithm to traverse from the initial idle state to state 2 to kickstart the robot activities.
Lastly, 12 3000mAh Ni-MH rechargeable batteries are used to supply 14.4V which is stepped down to 12V by a DC-DC buck convertor (Full name)to power DC motors via motor driver. The 12V is then stepped down again to 5V to power the remaining electronics.
~2.3m

## Slide 10: System Block Diagram
Colour Sensing Subsystem
Puck Handling Subsystem
Movement Subsystem
State Sequence Initiation Subsystem
Fig. 1 System block diagram.
Fig. 12 Initial idle state and state 2 of state machine.
Fig. 13 PSoC 5LP prototyping kit (CY8CKIT-059) [8].
Reset button
Push button
State Sequence Initiation Subsystem
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Fig. 1 System block diagram.
Notes: To handle all aspects of tasks provided in this project, there are 4 main subsystems implemented in the robot which are colour sensing, puck handling, movement, and state sequence initiation subsystems.
First is about the colour sensing subsystem. Its algorithm outputs 2 types of signals to the 2 TCS3200 colour sensors, one to switch on and off the attached LEDs, the other is for activation of photodiodes with filter of different colours. The algorithm receives input signal of square wave with different frequency to determine puck colour.
Secondly, it’s about the puck handling subsystem. The algorithm outputs analogue signal of pulse width modulator compare value which represents the duty cycle for angular positioning of servo rod to any of the 4 SG90 plastic gear servo motors. The servo motor would then rotate its rod accordingly to flick puck.
Next is the movement subsystem. The algorithm sends signals to the motor driver to inform the intended rotating speed and direction of the wheels to move and stop the robot. The motor driver then outputs the information to the DC motors by changing voltage supplied. Each DC motor has its shaft attached to a gearbox which is connected to a wheel so that the DC motor shaft and the wheel has the same speed and direction. The shaft encoder attached to each DC motor can indirectly capture the angular displacement of the wheel. The signals are then fed back into the algorithm consistently to enable motion control, speed control and differential drive control.
The fourth is the state sequence initialization subsystem. A press of the reset button on the PSoC board signals the algorithm to reset the robot to be in the initial idle state. The push button can then be pressed to inform the algorithm to traverse from the initial idle state to state 2 to kickstart the robot activities.
Lastly, 12 3000mAh Ni-MH rechargeable batteries are used to supply 14.4V which is stepped down to 12V by a DC-DC buck convertor (Full name)to power DC motors via motor driver. The 12V is then stepped down again to 5V to power the remaining electronics.
~2.3m

## Slide 11
Colour Sensing Subsystem
Puck Handling Subsystem
Movement Subsystem
State Sequence Initiation Subsystem
Fig. 1 System block diagram.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Fig. 14 A 3000mAh Ni-MH rechargeable battery [9].
Fig. 15 LM2596 3A DC-DC adjustable step down voltage regular / buck convertor with display [10].
Power Supply
Fig. 1 System block diagram.
Notes: To handle all aspects of tasks provided in this project, there are 4 main subsystems implemented in the robot which are colour sensing, puck handling, movement, and state sequence initiation subsystems.
First is about the colour sensing subsystem. Its algorithm outputs 2 types of signals to the 2 TCS3200 colour sensors, one to switch on and off the attached LEDs, the other is for activation of photodiodes with filter of different colours. The algorithm receives input signal of square wave with different frequency to determine puck colour.
Secondly, it’s about the puck handling subsystem. The algorithm outputs analogue signal of pulse width modulator compare value which represents the duty cycle for angular positioning of servo rod to any of the 4 SG90 plastic gear servo motors. The servo motor would then rotate its rod accordingly to flick puck.
Next is the movement subsystem. The algorithm sends signals to the motor driver to inform the intended rotating speed and direction of the wheels to move and stop the robot. The motor driver then outputs the information to the DC motors by changing voltage supplied. Each DC motor has its shaft attached to a gearbox which is connected to a wheel so that the DC motor shaft and the wheel has the same speed and direction. The shaft encoder attached to each DC motor can indirectly capture the angular displacement of the wheel. The signals are then fed back into the algorithm consistently to enable motion control, speed control and differential drive control.
The fourth is the state sequence initialization subsystem. A press of the reset button on the PSoC board signals the algorithm to reset the robot to be in the initial idle state. The on-board push button can then be pressed to inform the algorithm to traverse from the initial idle state to state 2 to kickstart the robot activities.
Lastly, 12 3000mAh Ni-MH rechargeable batteries are used to supply 14.4V which is stepped down to 12V by a DC-DC buck convertor to power DC motors via motor driver. The 12V is then stepped down again to 5V to power the remaining electronics.
~2.3m

## Slide 12
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making

## Slide 13: Crucial Aspects of Design
Shortest route movement strategy
  Shortest movement time to visit all the zones
  Move forwards and backwards only
  No point turning
4 servo motor puck flicking mechanism
  Each servo motor is responsible to each puck
  Start accumulating points right after zones visiting with no additional robot movement
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Crucial Aspects of Design
Notes: There is something interesting that the system block diagram cannot show, the crucial aspects of the design.
This competition requires a fast and reliable robot to shift as many pucks as possible in a limited period. Therefore, to ensure shortest movement time and shortest travelled distance to visit all the collection zones, the robot moves forwards straight into the collection zones at the beginning. The robot then only moves forwards and backwards in the 4 collection zones which saves movement time since it takes longer for movement if the robot needs to enter free zone. This movement strategy involves no point turning which lifts the burden of robot alignment. This is made possible by using 4 servo motor puck flicking mechanism. Each servo motor is attached to each corner of the chassis to be responsible for the puck in each collection zone. Besides, since the robot stays between the pucks after visiting all collection zones, this flicking mechanism allows immediate point accumulation with no extra movement.
These designs mainly are to reduce the movement time to leave more time for point accumulation.
~1.1m

## Slide 14: Crucial Aspects of Design
Shortest route movement strategy
  Shortest movement time to visit all the zones
  Move forwards and backwards only
  No point turning
4 servo motor puck flicking mechanism
  Each servo motor is responsible to each puck
  Start accumulating points right after zones visiting with no additional robot movement
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Notes: There is something interesting that the system block diagram cannot show, the crucial aspects of the design.
This competition requires a fast and reliable robot to shift as many pucks as possible in a limited period. Therefore, to ensure shortest movement time and shortest travelled distance to visit all the collection zones, the robot moves forwards straight into the collection zones at the beginning. The robot then only moves forwards and backwards in the 4 collection zones which saves movement time since it takes longer for movement if the robot needs to enter free zone. This movement strategy involves no point turning which lifts the burden of robot alignment. This is made possible by using 4 servo motor puck flicking mechanism. Each servo motor is attached to each corner of the chassis to be responsible for the puck in each collection zone. Besides, since the robot stays between the pucks after visiting all collection zones, this flicking mechanism allows immediate point accumulation with no extra movement.
These designs mainly are to reduce the movement time to leave more time for point accumulation.
~1.1m

## Slide 15
Shortest Route Movement Strategy
 Move forwards and backwards only
 No point turning
Fig. 16 Shortest route movement strategy.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making

## Slide 16
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Shortest Route Movement Strategy
 Move forwards and backwards only
 No point turning
Fig. 16 Shortest route movement strategy.

## Slide 17
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Shortest Route Movement Strategy
 Move forwards and backwards only
 No point turning
Fig. 16 Shortest route movement strategy.

## Slide 18
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Shortest Route Movement Strategy
 Move forwards and backwards only
 No point turning
Fig. 16 Shortest route movement strategy.

## Slide 19: Crucial Aspects of Design
Shortest route movement strategy
  Shortest movement time to visit all the zones
  Move forwards and backwards only
  No point turning
4 servo motor puck flicking mechanism
  Each servo motor is responsible to each puck
  Start accumulating points right after zones visiting with no additional robot movement
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Notes: There is something interesting that the system block diagram cannot show, the crucial aspects of the design.
This competition requires a fast and reliable robot to shift as many pucks as possible in a limited period. Therefore, to ensure shortest movement time and shortest travelled distance to visit all the collection zones, the robot moves forwards straight into the collection zones at the beginning. The robot then only moves forwards and backwards in the 4 collection zones which saves movement time since it takes longer for movement if the robot needs to enter free zone. This movement strategy involves no point turning which lifts the burden of robot alignment. This is made possible by using 4 servo motor puck flicking mechanism. Each servo motor is attached to each corner of the chassis to be responsible for the puck in each collection zone. Besides, since the robot stays between the pucks after visiting all collection zones, this flicking mechanism allows immediate point accumulation with no extra movement.
These designs mainly are to reduce the movement time to leave more time for point accumulation.
~1.1m

## Slide 20: 4 servo puck flicking mechanism
Each servo motor is responsible to each puck
Start accumulating points right after zones visiting with no additional robot movement
Fig. 17 Bottom view of the robot.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making

## Slide 21
4 servo puck flicking mechanism
 Each servo motor is responsible to each puck
 Start accumulating points right after zones visiting with no additional robot movement
Fig. 18 4 servo puck flicking mechanism.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making

## Slide 22: Crucial Aspects of Design
Shortest route movement strategy
  Shortest movement time to visit all the zones
  Move forwards and backwards only
  No point turning
4 servo motor puck flicking mechanism
  Each servo motor is responsible to each puck
  Start accumulating points right after zones visiting with no additional robot movement
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Notes: There is something interesting that the system block diagram cannot show, the crucial aspects of the design.
This competition requires a fast and reliable robot to shift as many pucks as possible in a limited period. Therefore, to ensure shortest movement time and shortest travelled distance to visit all the collection zones, the robot moves forwards straight into the collection zones at the beginning. The robot then only moves forwards and backwards in the 4 collection zones which saves movement time since it takes longer for movement if the robot needs to enter free zone. This movement strategy involves no point turning which lifts the burden of robot alignment. This is made possible by using 4 servo motor puck flicking mechanism. Each servo motor is attached to each corner of the chassis to be responsible for the puck in each collection zone. Besides, since the robot stays between the pucks after visiting all collection zones, this flicking mechanism allows immediate point accumulation with no extra movement.
These designs mainly are to reduce the movement time to leave more time for point accumulation.
~1.1m

## Slide 23: 02 Design Methodology
Motion Flow & Key Methods
Movement mechanism
Puck Handling mechanism
Colour Sensing mechanism
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making

## Slide 24
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
5
6
7
8
Fig. 19 Motion flow.

## Slide 25
5
6
7
8
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Fig. 19 Motion flow.
Notes: The robot then moves forwards straight into the puck collection zones 5 and 6 to have the pucks under the colour sensors. The forward movement and stopping at the right position make use of the movement mechanism.
~0.3m

## Slide 26: Movement Mechanism (Mechanical & Electronics)
Puck Handling Subsystem
Gearbox
DC motor with attached shaft encoder
Wheel
Spinning rod
Fig. 11 Wheel set.
Wheel set
Motor driver
PSoC microcontroller
Fig. 20 Bottom and top views of the robot.
Puck Handling Subsystem
Gearbox
DC motor with attached shaft encoder
Wheel
Spinning rod
Fig. 11 Wheel set.
Fig. 9 L298N motor driver [6].
Direction (IN1&IN2 or IN3&IN4), Speed (ENA or ENB)
Speed & direction (OUT1&OUT2 or OUT3&OUT4)
Fig. 10 Transfer plate [7].
Fig. 13 PSoC 5LP prototyping kit (CY8CKIT-059) [8].
Travelled distance (Phase A & Phase B)
Light output phases
Motor driver
PSoC microcontroller
Fig. 20 Bottom and top views of the robot.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Castor ball
Notes: As mentioned, each wheel in the wheel set has the same speed and direction as its DC motor. Each shaft encoder communicates with the PSoC microcontroller via a transfer plate while each DC motor does so via a motor driver. There is a pair of castor balls for third and fourth points of contact for stability and smooth movement of the robot.
~0.7m

## Slide 27: Movement Mechanism (Software)
Travelled distance feedback
Motion control
  Straight-line motion
  Stop movement
Speed control
Proportional controller for differential drive mechanism
Fig. 21 Movement Subsystem.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Notes: The movement algorithm can acknowledges travelled distance, conducts motion control, speed control and differential drive mechanism.
~0.2m

## Slide 28: Travelled Distance Feedback
Puck Handling Subsystem
Gearbox
DC motor with attached shaft encoder
Wheel
Spinning rod
Fig. 11 Wheel set.
Fig. 10 Transfer plate [7].
Fig. 13 PSoC 5LP prototyping kit (CY8CKIT-059) [8].
Travelled distance (Phase A & Phase B)
Light output phases
Fig. 22 Top-level schematics of the movement subsystem.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Notes: The movement algorithm inputs 2 signals phase A and phase B from each shaft encoder to acknowledge the angular displacement of each wheel. These inputs are connected to a quadrature encoder component in the PSoC creator whose count can represent travelled distance of each wheel. Let’s see how the quadrature encoder works physically.
~0.4m

## Slide 29: (Quadrature) Shaft Encoder
State diagram for forward motion |  | 
Light Phase | “A” Output | “B” Output
1 | 0 | 0
2 |  | 
3 |  | 
4 |  | 
“B” light
“A” light
Transmitters
Receivers
Light chopping disc
Fig. 23 Quadrature encoder and its wheel [11].
Wheel
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Notes: A shaft encoder has light transmitters, receivers and a light chopping disc as shown. The transmitters emit fixed light beam A and B to the disc and the corresponding receiver receives the light beam when the light is not blocked by a black spot of the disc. When a wheel keeps rotating, so does the encoder disc. This is reflected by changing light phases output. Thus, the movement algorithm can inputs the light phases output A and B constantly to compute the travelled distance of the wheel constantly for acknowledgement of robot position.
Optical Encoder (mit.edu)
~0.9m

## Slide 30: (Quadrature) Shaft Encoder
State diagram for forward motion |  | 
Phase | “A” Output | “B” Output
1 | 0 | 0
2 | 0 | 1
3 |  | 
4 |  | 
“B” light
“A” light
Transmitters
Receivers
Light chopping disc
Wheel
Fig. 23 Quadrature encoder and its wheel [11].
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making

## Slide 31: (Quadrature) Shaft Encoder
State diagram for forward motion |  | 
Phase | “A” Output | “B” Output
1 | 0 | 0
2 | 0 | 1
3 | 1 | 1
4 |  | 
“B” light
“A” light
Transmitters
Receivers
Light chopping disc
Wheel
Fig. 23 Quadrature encoder and its wheel [11].
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making

## Slide 32: (Quadrature) Shaft Encoder
State diagram for forward motion |  | 
Phase | “A” Output | “B” Output
1 | 0 | 0
2 | 0 | 1
3 | 1 | 1
4 | 1 | 0
“B” light
“A” light
Transmitters
Receivers
Light chopping disc
Wheel
Fig. 23 Quadrature encoder and its wheel [11].
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making

## Slide 33: Motion Control
Puck Handling Subsystem
Gearbox
DC motor with attached shaft encoder
Wheel
Spinning rod
Fig. 11 Wheel set.
Fig. 9 L298N motor driver [6].
Fig. 13 PSoC 5LP prototyping kit (CY8CKIT-059) [8].
Direction (IN1&IN2 or IN3&IN4), Speed (ENA or ENB)
Speed & direction (OUT1&OUT2 or OUT3&OUT4)
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Notes: Besides, the algorithm also controls 3 motions, stopping, rotating clockwise and anticlockwise of each wheel by adjusting the pair of binary bits IN1 IN2 or IN3 IN4. The 2 wheels rotate in the same direction for the robot to move forward and backward.

## Slide 34: Speed Control
Fig. 22 Top-level schematics of the movement subsystem.
Puck Handling Subsystem
Gearbox
DC motor with attached shaft encoder
Wheel
Spinning rod
Fig. 11 Wheel set.
Fig. 9 L298N motor driver [6].
Fig. 13 PSoC 5LP prototyping kit (CY8CKIT-059) [8].
Direction (IN1&IN2 or IN3&IN4), Speed (ENA or ENB)
Speed & direction (OUT1&OUT2 or OUT3&OUT4)
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Notes: Thirdly, the algorithm can vary the output pwm duty cycle to the enable pin to change speed of a wheel. Each wheel has 1 respective enable pin on the motor driver.

## Slide 35: Movement Subsystem (Software)
Fig. 21 Movement Subsystem.
Travelled distance feedback
Motion control
  Straight-line motion
  Stop movement
Speed control
Proportional controller for differential drive mechanism
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Notes: These 3 basic functions, acknowledgement of travelled distance, speed control, and motion control enable differential drive mechanism.

## Slide 36: Proportional Controller for Differential Drive
Colour Sensing Mechanism
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Puck Handling Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Kp = 250 (Stop at -3770)
Count error margin < 10
Movement Mechanism
Fig. 24 Flow diagram of the differential drive mechanism.
Fig. 25 Parameters of Pulse Width Modulator (PWM) for the motors.
Notes: The 2 wheels tend to have different physical speed despite same coded speed due to physical limitations. Therefore, the algorithm uses proportional controller for the differential drive mechanism to align speed of both wheels for smooth robot movement.
Before starting, we chose the right wheel to be the master wheel and the left to be the slave wheel. Speed of master wheel never changes while the speed of slave wheel is tuned constantly.
At first, we initialize shaft encoder count of both wheels to be 0.
Next is to define the proportional gain to be 250 which is obtained by trials and errors as too large the value oscillates the control output while too small the value induces slow response.
We then set both PWM compare values which reflects speeds to be 8000 initially which represents 32% duty cycle for a period of 25ms.
After then, the algorithm checks if the intended position is reached. If the condition is not met, the algorithm acquires the wheel counts and adjusts the speed of the slave wheel by changing the corresponding PWM compare value according to the equation shown. If the master wheel moves faster than the slave wheel at an instant, its wheel count must be larger and thus increases the speed of the slave wheel right after this instant to compensate the difference in travelled distance between the wheels. If the opposite happens, the speed of the slave wheel would be decreased. After 10 milliseconds, the process repeats until the intended wheel count is reached where the robot would stop movement.
The key movement methods are done and let’s get back to the robot motion flow.

## Slide 37
5
6
7
8
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Fig. 19 Motion flow.
Notes: The robot then moves forwards straight into the puck collection zones 5 and 6 to have the pucks under the colour sensors. The forward movement and stopping at the right position make use of the movement mechanism.
~0.3m

## Slide 38: Colour Sensing Mechanism (Electronics)
2 TCS3200 colour sensors for simultaneous colour sensing
64 photodiodes each with a filter | 
Filter | Number of photodiodes
Red | 16
Blue | 16
Green | 16
Clear (None) | 16
Fig. 2 TCS3200 colour sensor [1].
Fig. 20 Bottom and top views of the robot.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Colour Sensing Mechanism
Puck Handling Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Notes: Jual GY-31 TCS3200 Color Sensor Module (jogjarobotika.com)
TCS3200 Colour Sensor Module - Elecrow
The colour sensor has a 8x8 array of photodiodes with different type of filters. 16 of them have red filters, the same number goes to blue, green and clear filters.
~1m

## Slide 39: Red Puck Example
*The same logic is also valid for blue and green pucks!
Fig. 26 Front view of the robot with a red puck under one of the colour sensors.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Colour Sensing Mechanism
Puck Handling Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Notes: Jual GY-31 TCS3200 Color Sensor Module (jogjarobotika.com)
TCS3200 Colour Sensor Module - Elecrow
The colour sensor has a 8x8 array of photodiodes with different type of filters. 16 of them have red filters, the same number goes to blue, green and clear filters. Let’s assume a red puck is under the colour sensor. When the LEDs illuminate the red puck, the red puck tends to reflect higher irradiance of red component of light to the photodiodes with red filter which only receives red component of reflected light. This causes the current passing through the red photodiode to be higher compared to other photodiodes. The larger current is converted proportionally to a digital square wave at the output to the microcontroller with a larger frequency. The same logic is also valid for blue and green pucks. We can now move on to the algorithm.
~1m

## Slide 40: Red Puck Example
Fig. 3 TCS3200 colour sensor block diagram [2].
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Colour Sensing Mechanism
Puck Handling Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Notes: Jual GY-31 TCS3200 Color Sensor Module (jogjarobotika.com)
TCS3200 Colour Sensor Module - Elecrow
The colour sensor has a 8x8 array of photodiodes with different type of filters. 16 of them have red filters, the same number goes to blue, green and clear filters. Let’s assume a red puck is under the colour sensor. When the LEDs illuminate the red puck, the red puck tends to reflect higher irradiance of red component of light to the photodiodes with red filter which only receives red component of reflected light. This causes the current passing through the red photodiode to be higher compared to other photodiodes. The larger current is converted proportionally to a digital square wave at the output to the microcontroller with a larger frequency. The same logic is also valid for blue and green pucks. We can now move on to the algorithm.
~1m

## Slide 41: Colour Sensing Mechanism (Software)
Fig. 28 Top-level schematics of the colour sensing subsystem.
(PWM repeats)
Fig. 29 Counter captures number of output waves.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Colour Sensing Mechanism
Puck Handling Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Fig. 27 Flow diagram of the colour sensing mechanism.
Output frequency
(OUT)
Fig. 13 PSoC 5LP prototyping kit (CY8CKIT-059) [8].
LEDs on and off
(LED)
Output frequency scaling (S0 & S1)
Photodiode type
(S2 & S3)
Notes: The algorithm starts by activating the LEDs and the scaling pins for large enough output frequency and easier computation. After then, the photodiodes with red filter are activated.
//The PWM starts the fixed time window where the counters starts to count the rising edge of the sensor output wave. Two counters are used in the software for simultaneous colour sensing.
Once the fixed time window ends, the counters stop capturing the output wave and the output wave frequency is stored in the algorithm. The same process repeats for blue and green photodiodes. This flow shown here is then repeated 3 times and an average is taken for higher accuracy. The highest average frequency would determine the puck colour.
The colour sensing method is now clear and let’s get back to the motion flow of the robot.
~1m20s

## Slide 42
5
6
7
8
Fig. 19 Motion flow.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Colour Sensing Mechanism
Puck Handling Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Notes: Colour sensing is then done. The puck at zone 6 is valid and the robot will then attempt to flick it.

## Slide 43
Colour Sensing Mechanism
5
6
7
8
Fig. 19 Motion flow.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism
Notes: The motor first moves forwards for a certain distance.

## Slide 44
Colour Sensing Mechanism
5
6
7
8
Fig. 19 Motion flow.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism
Notes: To close the back servo rods.

## Slide 45
Colour Sensing Mechanism
5
6
7
8
Fig. 19 Motion flow.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism
Notes: It then moves backwards to the center between the pucks,

## Slide 46
Colour Sensing Mechanism
6
5
7
8
Fig. 19 Motion flow.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism
Notes: And flicks the valid puck. This puck shifting activity is made possible by the puck handling subsystem.

## Slide 47: 4 servo puck flicking mechanism
Colour Sensing Mechanism
Each servo motor is responsible to each puck
Start accumulating points right after zones visiting with no additional robot movement
Fig. 17 Bottom view of the robot.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism

## Slide 48
Colour Sensing Mechanism
4 servo puck flicking mechanism
 Each servo motor is responsible to each puck
 Start accumulating points right after zones visiting with no additional robot movement
Fig. 18 4 servo puck flicking mechanism.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism

## Slide 49: Puck Handling Mechanism (hardware & electronics)
Colour Sensing Mechanism
Fig. 4 Input and output pins of SG90 plastic gear servo motor [3].
(for angular displacement of servo rod)
Fig. 6 180-degree SG90 plastic gear servo motor [4].
Fig. 7 Servo motor with a rod attached.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism
Fig. 30 Servo rods.
Notes: Each servo is connected to a rod via xxx. The rod is made of yyy. The servo has an input pin connected to the microcontroller for the puck handling algorithm to instruct rotation of shaft and thus the rod.

## Slide 50: Puck Handling Mechanism (Software)
Colour Sensing Mechanism
6
5
7
8
~5.5cm
Dragging track
Fig. 31 If the servo rod drags the valid puck.
6
5
7
8
Flicking track
~xx deg
Fig. 32 If the servo rod flicks the valid puck.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism
Notes: For each servo rod, the distance between the pivot and the point of contact of the puck is roughly 5.5cm. Since the distance is not large enough for dragging action, flicking is used. The angular displacement of the servo rod to flick puck into the capture zone is roughly xx deg which is obtained by trials and errors.

## Slide 51: Puck Handling Mechanism (Software)
Colour Sensing Mechanism
2-output PWM
Fig. 33 Top-level schematics of the puck handling subsystem.
Fig. 4 Input and output pins of SG90 plastic gear servo motor [3].
Fig. 34 PWM_servo78 and PWM_servo56 signals.
(50kHz)
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism
Notes: How Servo Motors Work | Servo Motors High Efficiency and Power (jameco.com)
The puck handling algorithm makes use of 2 2-output PWM to control the angular position of the servo rods by changing corresponding PWM compare value. PWM compare value represents the PWM pulse width or the duty cycle. Increasing the duty cycle rotates the rod to one direction while decreasing rotates the rod to the other direction. As a PWM period of 50kHz is used, change of pulse width by 1ms rotates the servo rod by 180 degrees. For less than 180 degree rotation, the pulse width change is scaled accordingly. The puck handling algorithm thus rotates the servo rod whenever needed according to the motion flow.
~1m45s

## Slide 52
Colour Sensing Mechanism
5
6
7
8
Rod flicked, Rod stays
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism
Fig. 19 Motion flow.
Notes: Once the 2 second period is over, the servo rod retracts.

## Slide 53
Colour Sensing Mechanism
5
6
7
8
Rod retracts, Robot waits
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism
Fig. 19 Motion flow.
Notes: The system integrator can then placed back the captured puck into the black circle. Since no puck detection sensor is used, the robot depends solely on a delay of 8s to ensure the system integrator is able to placed the puck back before robot continues its activities.

## Slide 54
Colour Sensing Mechanism
5
6
7
8
Finished a puck capture by “flick, stay, retract and wait”
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism
Fig. 19 Motion flow.

## Slide 55
Colour Sensing Mechanism
5
6
7
8
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism
Fig. 19 Motion flow.
Notes: The robot then moves forwards to zones 7 and 8 for colour detection of the pucks.

## Slide 56
Colour Sensing Mechanism
5
6
7
8
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism
Fig. 19 Motion flow.
Notes: After colour detection, the robot moves backwards to the center between the pucks.

## Slide 57
Colour Sensing Mechanism
5
6
7
8
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism
Fig. 19 Motion flow.
Notes: The robot then flicks the valid puck at zone 7. Again, the servo rod retracts after 2 seconds.

## Slide 58
Colour Sensing Mechanism
5
6
7
8
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism
Fig. 19 Motion flow.
Notes: The robot then flicks the valid puck at zone 7. Again, the servo rod retracts after 2 seconds.

## Slide 59
Colour Sensing Mechanism
5
6
7
8
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism
Fig. 19 Motion flow.
Notes: The system integrator then has 8 seconds to place back the valid puck.

## Slide 60
Colour Sensing Mechanism
5
6
7
8
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism
Fig. 19 Motion flow.
Notes: The system integrator then has 8 seconds to place back the valid puck. The robot has managed to visit all the zones and it stays stationary from now on to accumulate points.

## Slide 61
Colour Sensing Mechanism
5
6
7
8
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism
Fig. 19 Motion flow.
Notes: The cycle of flicking and puck replacement focusing on a valid puck repeats until the end of the half round.

## Slide 62
Colour Sensing Mechanism
5
6
7
8
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism
Fig. 19 Motion flow.

## Slide 63
Colour Sensing Mechanism
5
6
7
8
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Puck Handling Mechanism
Fig. 19 Motion flow.

## Slide 64: 03 Decision Making
Unused Alternative Design
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making

## Slide 65: Unused Alternative Design
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Visit collection zones one by one
  Longer route & time needed
Point turning
  Alignment / reorientation needed
Possible extra movement
  Longer route & time needed
Fig. 35 Unused alternative design.

## Slide 66: Unused Alternative Design
Visit collection zones one by one
  Longer route & time needed
Fig. 35 Unused alternative design.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Approximate Travel Distance (Count) To Visit All Collection Zones Excluding Point Turning | Shaft Encoder Count Before Puck Accumulation Assuming A Valid Puck at Zone 7 | 
Movement to Any Collection Zone | Alternative Design | Current Design
Starting Base to One Zone | 2200 | 2200
To Next Zone | 2000 | -
To Next Zone | 5000 | 2000
To Next Zone | 2000 | -
Total | 11200 | 4200
Notes: Next is about our alternative design. We have been trying to improve our design of the robot and the motion flow that we have thought of many different design. One major alternative is a rather conventional robot as shown.
Only 2 servo motors and 1 colour sensor are used. This signifies that the robot has to go through all collection zones one by one to visit them.
In addition, the movement involves point turning which increases the risk of robot misalignment and requires reorientation mechanism by pushing limit switches against the wall after every point turning. The reorientation process demands time in the competition as well as from us to learn to apply the switches by ourselves.
Moreover, since there is no simultaneous colour sensing mechanism, the robot also needs more time for colour sensing.
Fourthly, the robot cannot stay stationary for point accumulation which introduces more uncertainty and more power needed.
Lastly, if it turns out that zones5 and 7 have no valid puck, the robot needs to move an even longer route to start accumulating points.
In other words, the alternative design is no much simpler although it involves less servo motors and colour sensors, it uses limit switches which we never used before. In addition, the alternative design takes a longer time to visit all the zones before starting accumulating points compared to our current design. As a result, the alternative design is not used.

## Slide 67
Visit collection zones one by one
 Longer route & time needed
Fig. 36 Motion flow of alternative design.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
5
6
7
8
5
6
7
8
Approximate Travel Distance (Count) To Visit All Collection Zones Excluding Point Turning | Shaft Encoder Count Before Puck Accumulation Assuming A Valid Puck at Zone 7 | 
Movement to Any Collection Zone | Alternative Design | Current Design
Starting Base to One Zone | 2200 | 2200
To Next Zone | 2000 | -
To Next Zone | 5000 | 2000
To Next Zone | 2000 | -
Total | 11200 | 4200
Fig. 19 Motion flow of our current design.

## Slide 68
5
6
7
8
Point turning
 Alignment / reorientation needed
Fig. 36 Motion flow of alternative design.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making

## Slide 69
5
6
7
8
Point turning
 Alignment / reorientation needed
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Fig. 36 Motion flow of alternative design.

## Slide 70
5
6
7
8
Point turning
 Alignment / reorientation needed
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Fig. 36 Motion flow of alternative design.

## Slide 71
5
6
7
8
Point turning
 Alignment / reorientation needed
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Fig. 36 Motion flow of alternative design.

## Slide 72
5
6
7
8
Point turning
 Alignment / reorientation needed
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Fig. 36 Motion flow of alternative design.

## Slide 73: Unused Alternative Design
Visit collection zones one by one
  Longer route & time needed
Point turning
  Alignment / reorientation needed
Possible extra movement
  Longer route & time needed
Fig. 35 Unused alternative design.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
Notes: Next is about our alternative design. We have been trying to improve our design of the robot and the motion flow that we have thought of many different design. One major alternative is a rather conventional robot as shown.
Only 2 servo motors and 1 colour sensor are used. This signifies that the robot has to go through all collection zones one by one to visit them.
In addition, the movement involves point turning which increases the risk of robot misalignment and requires reorientation mechanism by pushing limit switches against the wall after every point turning. The reorientation process demands time in the competition as well as from us to learn to apply the switches by ourselves.
Moreover, since there is no simultaneous colour sensing mechanism, the robot also needs more time for colour sensing.
Fourthly, the robot cannot stay stationary for point accumulation which introduces more uncertainty and more power needed.
Lastly, if it turns out that zones5 and 7 have no valid puck, the robot needs to move an even longer route to start accumulating points.
In other words, the alternative design is no much simpler although it involves less servo motors and colour sensors, it uses limit switches which we never used before. In addition, the alternative design takes a longer time to visit all the zones before starting accumulating points compared to our current design. As a result, the alternative design is not used.

## Slide 74
5
6
7
8
Possible extra movement
 Longer route & time needed
Fig. 36 Motion flow of alternative design.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
5
6
7
8
￣▽￣
I’m fat but I can start accumulating points immediately~
Fig. 19 Motion flow of current design.
>﹏<

## Slide 75: Unused Alternative Design
Visit collection zones one by one
  Longer route & time needed
Point turning
  Alignment / reorientation needed
Possible extra movement
  Longer route & time needed
Fig. 35 Unused alternative design.
System Block Diagram
Crucial Aspects of Design
Motion Flow & Key Methods
Movement Mechanism
Puck Handling Mechanism
Colour Sensing Mechanism
Unused Alternative
System Overview
Design Methodology
Decision Making
>﹏<
Notes: Next is about our alternative design. We have been trying to improve our design of the robot and the motion flow that we have thought of many different design. One major alternative is a rather conventional robot as shown.
Only 2 servo motors and 1 colour sensor are used. This signifies that the robot has to go through all collection zones one by one to visit them.
In addition, the movement involves point turning which increases the risk of robot misalignment and requires reorientation mechanism by pushing limit switches against the wall after every point turning. The reorientation process demands time in the competition as well as from us to learn to apply the switches by ourselves.
Moreover, since there is no simultaneous colour sensing mechanism, the robot also needs more time for colour sensing.
Fourthly, the robot cannot stay stationary for point accumulation which introduces more uncertainty and more power needed.
Lastly, if it turns out that zones5 and 7 have no valid puck, the robot needs to move an even longer route to start accumulating points.
In other words, the alternative design is no much simpler although it involves less servo motors and colour sensors, it uses limit switches which we never used before. In addition, the alternative design takes a longer time to visit all the zones before starting accumulating points compared to our current design. As a result, the alternative design is not used.

## Slide 76: Summary
Simple Yet Efficient
X long routes
X realignment
Stationary
=

## Slide 77: Thank you!

## Slide 78: Reference
[1] “GY-31 TCS3200 COLOR SENSOR MODULE.” JOGJAROBOTIKA. http://www.jogjarobotika.com/sensor- warna/1317-gy-31-tcs3200-color-sensor-module.html (accessed Oct. 13, 2021).
[2] ams AG, “TCS3200, TCS3210 Programmable Color Light-to-Frequency Converter,” TCS3200 datasheet, 2016.
[3] “SG90 Servo Motor Datasheet,” SG90 datasheet, 2021.
[4] “TOWER PRO SG90 9G – Miniature Servo Motor.” ELECTRONICA EMBAJADORES. https://www.electronicaembajadores.com/en/Productos/Detalle/MMSV002/motors-servo-motors-linear- actuators/servo-motors/tower-pro-sg90-9g-miniature-servo-motor (accessed Oct. 13, 2021).
[5] “Johnson Standard 130 Motor Green Miniature DC Motor with Encoder Mini motro 25g Shaft Dia 2mm.” Amazon. https://www.amazon.in/Johnson-Standard-130-Miniature-encoder/dp/B07372CWTZ (accessed Oct. 13, 2021).
[6] “2Amp 7V-30V L298N Motor Driver / Stepper Driver (2 Channels).” Cytron. https://my.cytron.io/p-2amp-7v-30v- l298n-motor-driver-stepper-driver-2-channels?r=1 (accessed Oct. 13, 2021).
[7] A. A. Mohanan, “Motor connections,” L298N datasheet, 2021.

## Slide 79: Reference
[8] “CY8CKIT-059.” Mouser Malaysia. https://my.mouser.com/ProductDetail/Cypress-Semiconductor/CY8CKIT- 059?qs=PhR8RmCirEblciDRmpiVDw%3D%3D (accessed Oct. 13, 2021).
[9] “Beston 4pcs AA 3000mAh Ni-MH Rechargeable Batteries.” Shopee. https://shopee.com.my/Beston-4pcs- AA-3000mAh-Ni-MH-Rechargeable-Batteries-i.139879612.2111664617?position=6 (accessed Oct. 13, 2021).
[10] “LM2596 3A Buck Module with Display.” Cytron. https://my.cytron.io/p-lm2596-3a-buck-module-with- display?r=1&gclid=CjwKCAjwx8iIBhBwEiwA2quaq3v3F6hXLGpGe9ybfT0OdBRwqcSm55jbO2NBUbKHs_kZ3i 3WsphPFBoCaL8QAvD_BwE (accessed Oct. 13, 2021).
[11] “Optical Encoder Project.” MIT.edu. https://groups.csail.mit.edu/mac/users/pmitros/encoder/ (accessed Oct. 13, 2021).
[12] A. A. Mohanan. ECE3091. Class Lecture, Topic: “Control.” School of Engineering, Monash University Malaysia, 2021.